# MODEL : DAVD-0110CS

# DASH Systems

Audio Video Distribution Amplifier

19” rack mount typed models

DAVD-0110SS (10CH, S-Video, Stereo)

DAVD-0110CS (10CH, Composite, Stereo)

Specifications

[General]	- Power requirement	AC 200V∼230V, 50/60Hz

- Power consumption	10W

- Dimensions		19”rack type, 1U

484(W) × 44(H) × 312(D) mm

- Operating temperature	0  to 50°C

- Humidity		10 to 90%

[Video] 		- TV system		NTSC, PAL, SECAM

- Input	DAVD-0110SS 	S-Video,  Din 4pin, 1 input

DAVD-0110CS 	Composite Video,  RCA or BNC, 1 input

Level	1Vp-p/75Ω

- Output 	DAVD-0110SS 	S-Video,  Din 4pin, 10 outputs

DAVD-0110CS 	Composite Video,  RCA or BNC,  10 outputs

Level	1Vp-p/75Ω

- Though out

- Freq. Response		±0.5dB, 30-10MHz

- Crosstalk 		-50dB at 3.58MHz

- Hum & noise      	-60dBm max.

[Audio] 		- Input    	Impedance	600Ω (RCA,   1 input)

Level		max. 15dBm

- Output   	Impedance	600Ω (RCA, 10 outputs)

Level		max. 15dB

- Though out

- Freq. Response			±0.1dB, 30-20KHz

[Front Panel]

- Power Switch

- Input : Input signal display LED

[Rear Panel]

- Video Input 		 1ch

- Video Through out	 1ch

- Video Outputs		10ch

- Audio Input 		 1ch

- Audio Through out	 1ch

- Audio Outputs		10ch

- Fuse

- Power Inlet 		220V / 110V

# Text boxes

Audio/Video D.A.

User’s Manual