# CNC Pipe Bending Machine

Controller

====================================================

# Model:  DCNC0332

# Software Version: DPBC V3.0

# DASH Systems

©1999, DASH SYSTEMS, All Rights Reserved

# Contents

1. Mechanical Specifications						-----------------------   5

2. Recommended Requirements for Optimal System			-----------------------   6

# 2.1. AC Servo Motor					-----------------------   6

2.2. Cylinder						-----------------------   6

2.3. Limit Switch						-----------------------   6

2.4. Sensor						-----------------------   6

2.5. Controller						-----------------------   7

3. Control Panel

3.1. Switch						-----------------------   8

3.2. Mode Selection					-----------------------   8

3.3. Editing Key						-----------------------   8

3.3.1. Alphanumeric Keys				-----------------------   8

3.3.2. Screen Scroll Keys				-----------------------   8

3.3.3. SHIFT Keys					-----------------------   8

3.3.4. Functional Keys				-----------------------   8

3.3.5. Directional keys				-----------------------   8

3.3.6. Enter					-----------------------   8

3.3.7. ESC					-----------------------   8

3.3.8. Short Cut keys 				-----------------------   8

3.3.9. Yes/No Selection  				-----------------------   8

# 3.4. Manual Mode Keys

3.4.1. Operation for Axes				-----------------------   9

3.4.2. Cylinder on/off Keys				-----------------------   9

# 4. Menu Screen

4.0. Preparation						-----------------------   9

4.0.1. Power on					-----------------------   9

4.0.2. Parameters					-----------------------  10

4.0.3. Main Screen					-----------------------  11

4.1. Data							-----------------------  11

4.2. Data Edit						-----------------------  12

4.2.1. FPB Data Input				-----------------------  13

1) Feed					-----------------------  14

2) Plane  				-----------------------  15

3) Bend					-----------------------  15

4) FW: Once Forward			-----------------------  16

5) ST : Once Stop				-----------------------  16

6) XM: Crossmove 		 		-----------------------  16

4.2.2. XYZ Data Input				-----------------------  16

4.2.3. Working Specifications				-----------------------  17

1) Channel Name				-----------------------  18

2) Bending Radius				-----------------------  18

3) Working Style				-----------------------  18

4) No. of X,Y,Z-Entries			-----------------------  18

5) Reverse Bending			-----------------------  18

6) Pipe Set Position			-----------------------  18

7) Pressure Interference Position		-----------------------  18

8) Bending Form Interference Position		-----------------------  18

9) Use Mandrel				-----------------------  18

10) Spring Back Compensation 		-----------------------  18

11) Once Forward				-----------------------  19

12) Diameter of Pipe			-----------------------  19

13) Thickness of Pipe			-----------------------  19

14) Length of Pipe				-----------------------  19

15) Elongation Compensation			-----------------------  19

16) Use Counter				-----------------------  19

17) Use Crossmove				-----------------------  19

18) Material				-----------------------  20

19) R1, R2 Change				-----------------------  20

20) Process Repeat Bending			-----------------------  20

21) Use Mandrel Lubricant			-----------------------  20

22) Use Seam Checker			-----------------------  20

23) Square Pipe				-----------------------  20

24) Use Loader				-----------------------  20

25) Discharge Type				-----------------------  20

26) Use Robot				-----------------------  20

27) Calculated?				-----------------------  20

28) No. of Processes			-----------------------  20

4.2.4. Spring Back Compensation File			-----------------------  21

4.2.5. Copy other Channel and Revise			-----------------------  21

4.2.6. Delete Channel				-----------------------  22

# 4.3. Floppy Disk

4.3.1. Read from Floppy				-----------------------  23

4.3.2. Write to Floppy 				-----------------------  23

4.3.3. Erase a Block of Floppy 			-----------------------  24

4.3.4. Initialize (Format)				-----------------------  24

# 4.4. Print Out

4.4.1. Selection of Print Items				-----------------------  25

4.4.2. Selecting Channel No. to be printed		-----------------------  25

4.4.3. Contents					-----------------------  25

# 5. Plan

5.1. Plan							-----------------------  25

5.2. Change						-----------------------  25

5.3. Case of Selecting “yes” 					-----------------------  26

5.4. Case of Selecting “no”					-----------------------  26

# 6. Operation

6.1. Preparation						-----------------------  26

6.2. Operation Mode					-----------------------  26

6.3. Operation Monitoring Screen				-----------------------  27

# 6.4. Manual Mode

1) Origin Check					-----------------------  27

2) Pipe Set Position		 			-----------------------  27

3) Axes Operation					-----------------------  27

4) Cylinder Operation				-----------------------  28

6.5. Auto Mode Operation					-----------------------  28

6.6. Step Mode Operation					-----------------------  29

6.7. Elongation Measurement Mode				-----------------------  30

6.8. Mode Switching					-----------------------  31

7. Emergency Stop							-----------------------  31

# 8. Error & Recovery

1) Feed Data Editing Error				-----------------------  32

2) Bend Data Editing Error				-----------------------  32

3) In/Out Devices Error				-----------------------  32

# 9. Emergency Stop & Recovery

1) Limit Switch & Emergency Switch			-----------------------  33

2) Servo Alarm					-----------------------  33

Appendix 1: Sequences in Squeeze					-----------------------  34

Appendix 2: Sequences in Complicated Squeezes				-----------------------  35

Appendix 3: Mechanical Parameters					-----------------------  36

Appendix 4: Monitoring Screen for Inputs & Axes			-----------------------  38

Appendix 5: Internal Connection of Controller				-----------------------  39

# 1. Mechanical Specifications

# Please fill out this sheet according to your machine

| Article | Specification |
| --- | --- |
| CNC Control Axes | Feed, Plane, Bend |
| Bending Capacity |  |
| Maximum Bending Radius | R1 |  |
|  | R2 |  |
| Maximum Pipe Length | With Mandrel |  |
|  | Without Mandrel |  |
| Bending Range | 0 – 190 dg |
| Plane Range | ± 360 dg |
| Process | Bending Points | Up to 31 |
|  | Squeeze | Each Process |
| Speed | Bend ( °/ sec) | Max. 257° |
|  | Feed ( mm/sec) | Max. 2443 mm |
|  | Plane ( °/ sec) | Max. 345° |
| Accuracy | Bend | ±0.05° |
|  | Feed | ±0.05mm |
|  | Plane | ±0.05° |
| Productivity |  |
| Memory | Onboard | 20 channels |
|  | Floppy Disk | 350 channels or 32 blocks |
| Motor | Hydraulic |  |
| Dimension |  |
| Weight |  |

# 2.  Recommended requirements for optimal system

2.1  AC Servo Motor

# Feed

Plane

Bend

2.2  Cylinder

Crossmove		:double operation

Mandrel     	:single operation

Pressure	  	:double operation

Upper Supporter	:double operation

Lower Supporter	:double operation

Table up/down	:double operation

Chuck  		:double operation

Clamp  		:single operation

# 2.3.  Limit switch

Feed		origin, end

Bend		end

# 2.4  Sensor

Clamp end sensor 		:  Checks if the clamp fixes the pipe to bending form.

Pressure origin sensor		:  Checks if the pressure arrives at the original position.

Pressure end sensor		:  Checks if the pressure entirely grips the pipe.

Table up sensor		:  Checks if the chuck carriage arrives at the upper R1 position.

Table down sensor		:  Checks if the chuck carriage arrives at the lower R2 position.

Chuck sensor			:  Checks if the chuck grips the pipe entirely.

Crossmove on sensor		:  Checks if the chuck carriage exits entirely from the center line of

bending form for feed or table movement.

Crossmove off sensor		:  Checks if the chuck carriage sits entirely on the center line of

bending form for bending.

Mandrel origin sensor		:  Checks if the mandrel arrives at the original position.

Mandrel end sensor		:  Checks if the mandrel arrives at the bending point.

Feed access sensor		:  Feed axis is decelerated when the controller checks this sensor in

order to stop accurately at the origin.

Feed origin sensor		:  Feed axis stops at this point when the controller checks this sensor

and the controller considers this the point of origin.

Plane origin sensor		:  Plane axis stops at this point when the controller checks this sensor

and the controller considers this the point of origin.

Bend access sensor		:  Bend axis is decelerated when the controller checks this sensor in

order to stop accurately at the origin.

Bend origin sensor		:  Bend axis stops at this point when the controller checks this sensor

and the controller considers this the point of origin.

# 2.5.  CONTROLLER

<< CONTROL  PANEL >>

[ Monitor ]

[ Operation & Editing Keys ]

# 3. Control Panel

# 3.1.  Switch

# Power

Motor		:  Servo Motor and Motor for Hydraulic

Emergency 	:  Emergency Stop

# 3.2  Mode selection

Auto run 	:  Mode in which a channel is executed automatically from start to finish..

Step run 	:  Mode in which a channel is executed step by step by pushing this key.

Manual 	:  Manual operation mode

Jog	:  Refer to the section: “Manual operation”

# 3.3. Editing keys

3.3.1  Alphanumeric keys

3.3.2  Screen scroll keys

Page up	   : Scrolls up one page.

Page down  :  Scrolls down one page.

3.3.3  Shift key

Left shift	:  Press this and one of the alphanumeric keys simultaneously to input a lower-left

character.

Right shift:  Press this and one of alphanumeric keys simultaneously to input a lower- right character.

3.3.4. Functional keys 	Ins :  Insert

Del :  Delete

Back space

3.3.5  Directional keys  :  To move the cursor or to select [y] or [n] in ”y/n” message boxes.

3.3.6.  Enter  :  To save data you input or to calculate FPB data.

3.3.7  ESC  :   To exit a Screen

3.3.8.  Short cut keys

# F1 :  Main Screen

F2 :  Plan

F3 :  Editing Channel Selection

F4 :  FPB Data Input

F5 :  XYZ Data Input

F6 :  Working Specification

F7 :  Initial Screen (to revise parameters)

3.3.9   Yes / No Selection

Yes  :   [Y] ,   [0]  or  the directional key at the message, “ y / n”

No   :   [N],   [1]  or  the directional key at the message, “ y / n”

# 3.4  Manual Mode Keys

3.4.1   Operation for Axes

Origin		:  To check the mechanical origin

P.S.P.           	:  To move the chuck carriage to the PIPE SET POSITION

Feed forward  	:  To move the chuck carriage forward along the feed axis.

Feed back     	:  To move the chuck carriage backwards along the feed axis

Plane left   	:  To rotate the plane axis counter-clockwise from the point of view of the

operator.

Plane right  	:  To rotate the plane axis clockwise from the point of view of the operator.

Bend  		:  To bend

Return 		:  To return the bending arm to the bend origin.

- Jog Mode ON

With Jog Mode ON, movements have no relation to the data from the channel.

Movement along the axes can be executed by pressing and holding the axes buttons.

- Jog Mode OFF

Movement along the axes can be achieved by pushing an axes button once to achieve movement in the

set increment.

3.4.2   Tighten / Loosen key ( on/off )		     [ Fig 0-1 Startup Screen ]

Chuck	 	: hold / release

Clamp	 	: hold / release

Table up/down 	: up / down

Pressure holding	: hold / release

Mandrel 		: on / off

Cross move 	: on / off

Supporter 1 	: up / down

Supporter 2 	: up / down

# 4. Menu Screen

# 4..0. Preparation

    - Power on

# After turning the power switch on [Fig 0-1 Startup Screen]

# appears on the CRT and then the message,

# “To get started, press [ENTER]”, appears at the bottom of [Fig 0-1 Startup Screen].

On pressing [ENTER], the screen shows:  		“Init.  System,  wait a second………………...”

“Serial No. :     DCNC******************.”

“To search for origin, Press [ENT]”

Pressing [ENTER] key again, the screen shows another message , “After safety check,  press [ENT]”.

After checking to make sure the machine is safe to operate press the [ENTER] key. The machine then

performs a test to find its mechanical origin.  The CRT displays the Main menu [Fig 0-6] after confirming the

origin point.

# Short cut key  F7:  Returns the operator to [Fig 0-1. Startup Screen] from any other screen.

4-0-2. Parameters   				     [ Fig 0-2. Parameter Setting ]

To set or change parameters, enter the password followed by

the [ENTER] key at [Fig 0-1. Startup Screen].

The Parameters screen will appear.

# You can return to the startup screen from any other screen

# by pressing the F7 key.

# 1) Mechanical parameters

Parameters are related to automatic operation.

Parameters include:

5 step speed settings for the three axes

delay time between operations and operation time

Enable/disable cylinder sensors

This screen is composed of 60 parameters as Fig 0-3,

Fig 0-4 and Fig 0-5. 				     [ Fig 0-3. Mechanical Parameter –1 ]

☞ [Refer to the Appendix 3. Mechanical parameters

for details.]

# 2) Axis Filter Adjustment:  Advanced Operator and Service

# Person Use Only

# 3) Input test :  To check the inputs, sensors, keys.

☞[Refer to the Appendix 4. Monitoring Screen for the details]

# 4) Change Password

This option is used to change the password.

The password must be 8 characters long.

# 5) Print Parameters : To print the present parameter settings.

[ Fig 0-4. Mechanical Parameter –2 ]   		     [ Fig 0-5. Mechanical Parameter –3 ]

4-0-3.  Main Screen  ( Short cut key : F1)	           [ Fig. 0-6.  Main screen ]

1. Data

- Data input

- Data revision

- Floppy Diskette

- Print out

2. Plan :  To set a working channel

3. Manual :  Manual Operation

4. Elon : Elongation Measurement

This is available in auto and step mode.

4.1.  Data

[ Fig 1-0. Selecting [Data] in Main Screen ]

4.1.0.  Select [Data] in the main screen with the arrow

keys or by pressing the [1] key, and the press

[ENTER] key.

[ Fig 1-1. Data ]

# 4.1.1.  Data  Menu

- Data edit :  Copy

Input

Revision

- Floppy :  Read a block from a floppy diskette

Write the active block #33 to a floppy

diskette.

Erase a block from a floppy diskette

Initialize a floppy diskette

- Print out : Data print

4.2..  Data Edit 	( Short Cut key: F3 )		     [ Fig 2. Editing Channel Selection ]

Selecting [Data Edit] in [Fig 1-1 Data],

the screen changes to [Fig 2. Editing Channel Selection].

# Press [Enter] key after entering the number of the channel

to edit. The screen changes to [Fig 2-0. Edit].

4.2.0.  Edit

# This screen is used to input bending data in the channel

selected at [Fig 2. Editing Channel Selection].

- Press the [Enter] key after inputting the item number to

be edited. The screen changes to display the item selected.

[ Fig 2-0. Edit ]

- FPB Data Input : Bending data (FEED, PLANE, BEND)

# You can work by inputting FPB. Data only without

# Inputting XYZ Data.

# Basically, this controls the machine through FPB data only.

# Furthermore the controller has the useful and convenient

# ability of being able to convert FPB data to XYZ. data.

- XYZ Data Input: Cartesian coordinates (X,Y,Z)

# If you input and save Cartesian (XYZ) data, Bending (FPB)

# data, is automatically calculated.

- Working Specifications :  Options

- Spring back compensation file

Spring back : 	Although a pipe is bent to the degree of bending called for in the data, it has the attribute of

returning back to its original shape to some extent because of its elasticity.

This phenomenon is called “Spring Back”.

Compensation:	The degree of bending needs to be set greater than the mathematical calculation in order to

compensate for this spring back.

Reference data : This spring backs are very different according to the materials involved, diameter and

bending degrees.  You can edit the reference table data according to experience or

experiment in advance so that spring back is compensated for automatically through

interpolation from the reference table.

- Copy other Channel and Revise :

It is possible to copy another channel, similar to the data you want to edit, to another channel and then

revise it.

- Delete this channel : To delete (clear) the selected channel.

# 4.2.1  FPB  Data Input  ( Short Cut key : F4 )

- Selecting [1] in the screen [Fig 2-0. Edit],               [ Fig 2-1  FPB Data Input ]

a [Fig 2-1 FPB Data Input] screen appears.

- Move the cursor to the next column with [Enter] or the

arrow keys after inputting data for a field or when not

making any revisions to a field.

-  If you come to this screen after inputting XYZ data,

The basic FPB data is already calculated and displayed.

All that is required is the input of speed(S), squeeze

type(?), squeeze data(SQ), spring back(SB), once

forward option(FW), once stop option(ST) and

crossmove option(XM)

# The data which has already been calculated can be

# revised.

If you come to this screen without inputting XYZ data,.								                 (fig 2-8  f,p,b  data input)

all of the FPB data must be inputted.

- FPB Data (Bending data)  : f : feed (mm)   p: plane (degree)   b: bend(degree)

The FPB data must be calculated incrementally, relative to the previous point.

# ☞- Converting  FPB data to XYZ data

You can convert Bending (FPB) data to Cartesian (XYZ) data.

- [INS] key :

Press [INS] key if you need to insert rows for more input data. A duplicate of the row on which the

cursor is located is inserted directly under that row.

- [DEL] key :

Press the [DEL] key to delete the row (process) on which the cursor is located.

- “R” : the number of the mold to be used [ the upper mold is 1, the lower mold is 2]

- “SB” :  spring back

If the option (10) “Spring Back Compensation” is set to “Y” (see [Fig 2-3-1 Pipe Working Specs].

and the spring back compensation file is already made, this is automatically calculated.

If the option (10) “Spring Back Compensation” is set to “N”, all of spring back data reads “0” and can

be revised manually..

- “FW”	 : once forward option for each process

- “ST”		: once stop option for each process

- “XM”	: crossmove option for each process

- “?”		: squeeze type for each feed, plane, bend

- “SQ”		: squeeze data for each squeeze type

- Pressing [ESC] key after inputting all the data, the message 	“Save changes?        y / n” appears.

Select “y” and the FPB data is saved with and the message 	“Generate XYZ data?   y / n ” appears.

# If XYZ data conversion is not needed, select “n” and the screen changes to [Fig 2-0 Edit] screen.

- How to convert FPB data to XYZ data

If XYZ data conversion is needed, select “y”.  The message “Revise first & final feed data?  y/n” appears.

Select “n”: no conversion will be made and the screen changes to [Fig 2-0 Edit] screen.

Select “y”: The data is converted to XYZ data. After the conversion is complete, the screen changes to

[Fig 2-2 XYZ Data Input] screen for checking the results.

If the channel already has XYZ data, the message  “Delete XYZ data and Regenerate! Y / n” appears.

Select “n”: conversion stops and the screen changes to [Fig 2-0 Edit] screen.

Select “y”: the screen changes to [Fig 2-2 XYZ Data Input] for deleting of the XYZ data.

Restart the conversion after deleting all of the XYZ data by pressing the [DEL] key in the screen

[Fig 2-2 XYZ Data Input].

# 1)  Feed

A.  S			:feed speed  (0-4)  	Five speed levels are available from level 0 to level 4.

These levels are set in the screen [Fig 0-3. Mechanical Parameter 1].

B. 	 F(mm):feed distance:  A distance from the present position to the next bend starting point in mm.

- First feed distance:

Negative value in Full working style:   After chucking pipe, the carriage feeds backward

Positive value in Full working style:    After chucking pipe, the carriage feeds forward

First feed in Process working style :    This distance is ignored.

- Final feed distance:

It should be inputted as a negative value.

If a positive value is inputted, the value is automatically changed to zero.

The carriage feeds backward unchucking the pipe before execution of the bending

operation of the final process

C.  ?			: squeeze type(0/1/2) 	To avoid interference between the bent section of the pipe and

bending form during rotation (PLANE).

☞			[Refer to the Appendix 1 and 2. “Sequence in Squeeze” for more information about squeeze type.]

0 :  normal action

1 :  The chuck carriage feeds by the sum of feed distance and feed squeeze distance.

The bending arm returns and the plane axis is rotated simultaneously.

Next, the chuck carriage feeds back by the feed squeeze distance.

2 : 	Full: 	The same as normal action.  After the normal action is complete, clamps pipe, unchucks

pipe, feeds back by feed squeeze distance, chucks pipe and finally bends.

Process :	This is basically the same as feed squeeze type 1 except the chuck carriage unchucks pipe

and feeds back by feed squeeze distance.

D.  SQ	:feed squeeze distance   a distance for the squeeze action in mm

# 2) Plane

A.  S			:plane speed (0-4)  Five speed levels are available from level 0 to level 4.

These levels are set in the screen [Fig 0-3. Mechanical Parameter 1].

B.  P(dg)	:plane angle	    The angle from present position to next bend starting position in degrees.

+:clockwise in view of an operator

- :counter-clockwise in view of an operator

C.  ?			:squeeze type (0/1)  To avoid interference between the bent section of the pipe and

bending arm during rotation (PLANE).

0 : 		Normal action

1 : 		Plane axis is rotated after the chuck carriage entirely feeds and bending arm entirely returns.

☞	[Refer to the Appendix 1 and 2. Sequence in Squeeze for the details of action sequences.]

# 3) Bend

A.  S			:bend speed  (0-4)   Five speed levels are available from level 0 to level 4.

These levels are set in the screen [Fig 0-3. Mechanical Parameter 1].

B.  B(dg)	:bend angle	      The angle from the bend origin in degrees

C.  ? 		: squeeze type (0/1/2)  To avoid interference between the bent section of the pipe and

bending arm during rotation (PLANE). or in feed movement

☞	[Refer to the Appendix 1 and 2. Sequence in Squeeze for the details of action sequences.]

0 : 		Normal action

1 : 		To avoid interference between the bent section of the pipe and bending arm during

rotation (PLANE). or in feed movement

Bend return to the squeeze angle, feed and plane are simultaneously operated.

After that, bend return to the origin is carried out.

2 : 		This function is for very large bend angles.

If bend squeeze type 2 is set, bending is divided in two steps.

First, bending is carried out according to the bend squeeze angle.

Pressure cylinder is loosened

Pressure cylinder is tightened again.

Finally, Bending is carried out according to the originally selected bend angle.

D. SQ(bend squeeze angle):   An angle for the squeeze action in degrees

This angle is always measured from the position of the origin. It is an absolute value.

E. SB(spring back): 	If the option (10) “Spring Back Compensation” is set to “Y” (see [Fig 2-3-1

Working Specs]). and the spring back compensation file is already made, this is automatically calculated.

If the option (10) “Spring Back Compensation” is set to “N”, all of spring back data reads “0” and can

be revised manually.  This angle is always the calculated from the present position.  It is a relative value.

# 4)  FW (once forward option of each process) :  To decide if the once forward option set in [Fig 2-3-1.

# Working Specifications 2] is used in each process or not.

If the once forward data set in [Fig 2-3-1. Working Specifications 2] is larger than feed data,

once forward option “y” is ignored.

And if the once forward option set in [Fig 2-3-1. Working Specifications 2] is ‘yes’,

“FW” of every processes is “no” but they can be changed to “yes”.

Otherwise, if the once forward option set in [Fig 2-3-1. Working Specifications 2] is ‘no’,

“FW” of every processes is “no” and they can not be changed to “yes”.

5) ST (once stop) :   a pause in a process

0 : 	no pause

1 : 	after feed

2 : 	after plane

3 : 	after bend

4 :   after crossmove cylinder is opened

# 6) XM (crossmove option of each process) : 	To decide if the crossmove option set in [Fig 2-3-1. Working

Specifications] is used in each process or not.

If the crossmove option 17) set in [Fig 2-3-1. Working Specifications] is ‘yes’,

“XM” of every process is “yes” but can be changed to “no”.

Otherwise, if the crossmove option 17) set in [Fig 2-3-1. Working Specifications] is ‘no’,

“XM” of every processes is “no” and can not be changed to “yes”.

4.2.2.  XYZ  Data Input  ( Short Cut key : F5 )

- Selecting [2] in the screen ]Fig 2-0. Edit], 		   [ Fig 2-2  XYZ Data Input ]

a [Fig 2-2 XYZ Data Input] screen appears..

- Move the cursor to the next column with [Enter] or the

arrow keys after inputting data for a field or when not

making any revisions to a field.

- [INS] key

A newly created channel has only one row or process.

Press the [INS] key if you need to insert rows for more

input data. A duplicate of the row on which the cursor is

located is inserted directly under that row.  The maximum

number of XYZ data processes is 32.

- [DEL] key :

# Press [DEL] key to delete the line on which the cursor is located.

- XYZ Data Input: Cartesian coordinates (X,Y,Z)

# If you input and save Cartesian (XYZ) data, Bending (FPB) data, is automatically calculated.

- “r” : the number of the mold to be used [ the upper mold is 1, the lower mold is 2]

- “j” : Use this option to omit a coordinate temporarily.

Although the coordinate is not a bending point, feed distance and arch length are calculated and

the sum of feed distance and arch length are added to the next feed..

- “@”	: This means 180degrees’ bending and it is not for input but automatically determined.

# If it is “y”, it means that the X,Y,Z coordinate and the next X,Y,Z coordinate are combined to be bent

180degrees. Therefore the two X,Y,Z coordinates become a bending point in FPB data.

- Pressing [ESC] key after inputting all data, the message 		“save changes?        y / n” appears.

Selecting  “y”, the message 			        “generate FPB data ?    y / n” appears.

Selecting  “y”, FPB data is produced and the screen changes to [Fig 2-1 FPB Data Input].

Selecting  “n”, the XYZ data is saved but FPB data is not generated.

And the screen changes to the screen, [Fig 2-0 Edit].

If the channel has already FPB data,  the message  		“already gen‘d! re-gen.? y /n” appears.

Selecting  “y”, FPB data is produced and the screen changes to the screen, [Fig 2-1 FPB Data Input].

Selecting  “n”, the XYZ data is saved but FPB data is not generated.

And the screen is changed to the screen, [Fig 2-0 Edit].

# 4.2.3.  Working Specifications  ( Short Cut Key  : F6 )

- This options is used to define production specifications, control operation orders, method and usage of each

component of the system.

- Selecting [3] in the screen [Fig 2-0. Edit], the screen [Fig 2-3-1.Working Specifications] appears.

- Move the cursor to the next column with [Enter] or the arrow keys after inputting data for a field or when not

making any revisions to a field.

- The channel number at the top of the screen indicates the channel being edited..

- The “feed” at upper-right indicates the current feed position.

It continually changes with movement along the feed axis,  so it is useful in determining the values of

6) pipe set position, 7) pressure interference position and 8) bending form interference position..

1) Channel Name : File Name		            [ Fig 2-3-1. Working Specifications ]

2) Bending R :  Radius of Bending Form

upper mold : 1,	lower mold : 2

3) Working Style :	 Process  “Y”  or  “0”

Full     “N”  or  “1”

* You may press “0” instead of “y” and “1” instead of “n”

in any screen of this program..

4) No. of XYZ data items: counted automatically and

displayed later

5) Reverse Bending

Used to reverse bending order, including start points and bending end points, of XYZ coordinate data.

This is available only when option 27) Calculated? is set to “Y”.

If XYX data is not inputted, this option is not available.

To use this option, convert FPB data to XYZ data and re-generate FPB data.

6) Pipe Set Position (Working Origin)

# Set a position to chuck a pipe by the distance from the mechanical origin.

Refer to the present feed position at the top of this screen.

This present feed value can be manually changed in jog mode with the feed forward/backward keys or by

moving the carriage by hand while the motor is off.  These changes should be entered into the Pipe Set

Position field manually.

# You can set option 7) and 8) interference positions in the same manner.

7) Pressure Interference Position (with chuck carriage)

This is the position at which the chuck carriage interferes with the pressure mold.

Set this position according to the distance from the mechanical origin.

This position is used to prevent the chuck carriage from colliding with the pressure mold by causing an

interference error.

8) Bending Form Interference Position (with chuck carriage)

This is the position at which the chuck carriage interferes with the bending form.

Set this position according to the distance from the mechanical origin.

This position is used to prevent the chuck carriage from colliding with the bending form by causing an

interference error.

9) Use Mandrel ? :  Indicates if a mandrel cylinder is used or not

10) Spring Back Compensate : Set to “y” if the spring back compensation file is applied for interpolation.

11) Once forward

The pipe may collide with clamp holder when bent in the lower mold of the bending form,R2.

You can avoid this collision by using this once forward option.

This option is used to divide the original feed distance into two parts.

As a result, the chuck carriage feeds forward by the “once forward option distance”, the bending arm returns

and finally the chuck carriage feeds forward completely.

# Set to “y” if this option is used and then set a distance.

12) Diameter of pipe 	: only for reference

13) Thickness of pipe 	: only for reference

14) Length of pipe    	: only for reference but the controller calculates and shows it in this column.

15) Elongation compensation

# To decide if the elongation during bending is compensated in the next feed movement or not.

“yes” :  To add the elongation to the next feed.

“no “ :  The elongation from every process is fed into the end of the pipe.

16) Use Counter ?

If the counter option is set to “y”, it compares the worked quantity (done) with total quantity of work to be

done (quantity) set in screen, [Fig 5-1. Plan].

# The operation jumps to the next item set in [Fig 5-1. Plan] when the quantity completed is equal

to the total quantity of work to be done set for this item.

# If the counter option is set to “n”. the working channel selected with the [INS] key is marked “*” and is

performed continuously.

17) Use Crossmove ? :  Used to decide if the crossmove cylinders are used or not.

-  YES : The process options for crossmove, XM, in [Fig. 2-2 FPB Data Input] are set to “y”.

And the XM process option can be changed to “NO” for each process in no relation to channel

option for crossmove.

# The actual operation is performed by the XM process option in [Fig 2-2 FPB Data Input].

-  NO : The process options for crossmove, XM, in [Fig 2-2 FPB Data Input] are set to “n”.

And the XM process option can not be changed to “YES” for each process.

# Use the [PAGE DOWN] key to move to the next options screen.

18) Material	:  To input material of pipe (only for reference)

[ Fig 2-3-2 Working Specifications 2]

19) R1, R2 Change :  To decide if the upper and the lower

mold of the bending form are used

simultaneously in bending a piece of pipe.

20) Process Repeat Bending

# To repeat bending from a process to another process.

- y/n  :  If this function is used or not : y/n

- from :  process no. from which a repeating cycle

starts

- to 	 :  process no. to which a repeating cycle ends.

- # 			: 	number of repetitions

21) Use Mandrel Lubricant :

# Determines if a mandrel lubricant is used or not.

22) Use Seam Checker : Determines if a seam (bead) checker is used or not.

(This option is not available on this model.  This item is for later versions of the controller.)

23) Square Pipe Working : 	If this option is set to “y”, the crossmove cylinders is automatically used so that

square pipe can be bent.

24) Use Loader?:  Determines if a pipe loader is used or not.

(This option is not available on this model.  This item is for later versions of the controller.)

25) Discharge Type : To set how to discharge the bent pipe in auto mode.

0 :  Auto operation stops in an unchucked state after bending of the final process..

Pressing “foot switch 1”,  the clamp cylinder is opened (unclamping).

Pressing “foot switch 2”,  the bending arm returns to its origin.

1 : 	 Auto operation stops in an unclamped state after bending of the final process..

Pressing “foot switch 2”,  the bending arm returns to its origin.

2 : Auto operation stops temporarily in an unclamped state after bending of the final process.

The bending arm automatically returns after a delay (kicker time) set in mechanical parameters

in advance.

26) Use Robot?	: To set if a robot is used for unloading pipes or not.

(This option is not available on this model.  This item is for later versions of the controller.)

27) Calculated ? :  This automatically shows if this channel has XYZ data and FPB data that was generated

from XYZ data.

28) no. of processes : This automatically shows how many processes are in the channel.

This number of processes is always one greater than the number of bending points.

Press [ESC] key after setting all of the options on this screen. The message, “save changes?  y / n” appears.

Select “y” and the data is saved and the screen returns to the screen [Fig 2-0. Edit].

4.2.4.  Spring Back Compensation File

- Select [4] in the screen, [Fig 2-0. Edit], 		     [ Fig 2-4. Spring Back Compensation File ]

a [Fig 2-4. Spring Back Compensation File] screen appears.

- Move the cursor to the next column with [Enter] or the arrow

keys after inputting data for a field or when not making any

revisions to a field.

- Spring back compensation file

Spring back : 	Although a pipe is bent to the degree of

bending called for in the data, it has the attribute of

returning back to its original shape to some extent

because of its elasticity. This phenomenon is called

“Spring Back”.

Compensation:	The degree of bending needs to be set

greater than the mathematical calculation in order

to compensate for this spring back.

Reference data : This spring backs are very different

according to the materials involved, diameter and bending degrees.

You can edit the reference table data according to experience or experiment in advance so that spring

back is compensated for automatically through interpolation from the reference table.

Pressing [ESC] key after inputting all data, the message 		“save changes?        y / n” appears.

Selecting  “y”, the spring back data is saved and the message	“data  saved!!!” appears.

Pressing [ENTER] or [ESC] key, the screen is changed to the screen [Fig 2-0 Edit].

If selecting “n”, the screen is changed to the screen [Fig 2-0 Edit] without saving data..

If you change a “spring back compensate” file, FPB data must be calculated again in the XYZ data input screen.

4.2.5.  Copy other Channel and Revise	     	           [ Fig 2-5-1 Copy ]

# You can copy any channel to another channel and revise it

if you find a channel similar to the data you want to edit

from block#33 or a block from a floppy disk.

- Selecting [5] in the screen [Fig 2-0. Edit], a screen

[Fig 2-5-1. Copy] appears.

- Block #33 indicates a block in the memory of the controller

itself .  Twenty channel names(channel names) are

displayed.

# The 32 block names on a floppy disk in the FDD

are displayed in the right side.

# If there is not a floppy disk in the FDD, the message “check

# your FDD” appears.

# You can ignore that message if you intend to copy from the memory of the controller itself.

# 1) [blk#]

When a block number is inputted at the column [blk#] in the last row, the 32 block names disappear and the

20	drawing names in that block are displayed.

Inputting “33” means you intend to copy a channel from the memory of the controller itself.

# 2) from [ch#] : Input a channel no. to copy from.

3) to [ch#] : 	Input a channel no. to copy to

# 4) Press [ENTER] key, the screen [Fig 2-5-2 Contents to Copy] appears.

[ Fig 2-5-2. Contents to Copy ]

[Contents to Copy]

Screen for selecting the contents to copy.

# 1)	At first, check the channel no. to copy from and the

channel no. to copy it to.

# 2)	Move the cursor to the articles you want to copy with the

numeric keys or the directional keys and press the [INS]

key.

# 3)	A “*” mark is displayed next to those items.

Press [INS] key once more to cancel.

Multiple articles can be marked.

# 4) Copying

Pressing [ENTER] key after completing steps 1-3 above.

The message “copy ok (y=0 / n=1)  y / n”  appears.

Select “y” and the CPU starts copying.  After copying is complete, the display automatically goes to the

screen, [Fig 2-0. Edit].   Select “n” to start the copying process over again.

4.2.6.  Delete Channel				   [ Fig 2-6  Delete This Channel ]

This menu item is used to delete an unnecessary channel in

the memory.

- Selecting [6] in the screen, [Fig 2-0. Edit],

the message “OK to delete ch #00?  y / n” appears.

- Select “y”: the CPU deletes the channel data,

after that, the message “ch #00 deleted! [ENT]” appears.

# Press [ENTER] and the display automatically goes to

the screen [Fig 2-0 Edit].

- Select “n”: the display automatically goes to the screen,

[Fig 2-0. Edit] without deleting.

# 4.3.  Floppy Disk

32 blocks or 350 channels can be saved on a floppy disk.    [ Fig 3-1. Floppy Disk ]

# 4.3.0.  Floppy Disk

# Select [2] in the screen [Fig 1-1 Data] and

a screen [Fig 3-1. floppy disk] appears.

# 4.3.1. Read from Floppy

# You can read a block from a floppy disk and

copy it to the memory of the controller itself.

# Selecting [1], a screen [Fig 3-2 Read from floppy]

appears and 32 blocks are displayed on the screen.

A message, “block no, ?” appears.

Input a block no. and press the [ENTER] key.

The message “ read from blk #00 ?  y /n “ appears.

Select “yes” and wait while the data is being read.

The message  “data read from block #**  !!!   [ret]” appears.

Pressing [ENTER], the screen returns to [Fig 3-1].	    [ Fig 3-2. Read from Floppy ]

# Caution!. 	: If a block is copied to the memory of the

# controller. 20 channels of data in the memory of

controller itself will be erased.

# Please write them to a floppy disk for back-up.

# 4.3.2.  Write to Floppy

# You can write 20 channels of data as a block to a floppy

# disk.

# Selecting [2], a screen [Fig 3-2 Write to Floppy]

appears and 32 blocks are displayed on the screen.

The message “block no, ?” appears.

Input a block no. and press the [ENTER] key,

the message “save in block #00 ?  y /n “ appears.

Select “yes” and wait while the data is being written.

The message “data saved in block #**  !!!   [ret] “ appears.

# Press [ENTER] and the screen returns to [Fig 3-1].

# Caution!.   If this function is run, 20 channels of data in a block of the floppy disk are erased.

# 4.3.3  Clear a Block in Floppy

You can delete a block from a floppy disk.

Select [3] and  a screen [Fig 3-2 Clear Block of Floppy] appears and 32 blocks are displayed on the screen.

A message, “block no, ?” appears.

Input a block number and press the [ENTER] key.  The message “clear block #00 ?  y /n “ appears.

Select “yes” and wait while the block is cleared.  The message “block #00 deleted!!!   [ret]“ appears.

# Press [ENTER] and the screen returns to [Fig 3-1].

# Caution!.  : Once a block has been cleared it can not be recovered.

# 4.3.4. Initialize (format)

# You must initialize a diskette when you use it in the controller for the first time.

Select [4] and the message “ initialize y/n ?” appears.

Select “yes” or “0” and the initialization starts.

After the initialization is completed, the screen returns to [fig 3-1].

# 4.4  Print out

This menu is used to print data from the memory of the controller itself.

Select [3] in [Fig 1-1 Data] and the screen [Fig 4-1 Print out] appears.

4.4.1. Selection of printing items			    [ Fig 4-1 Print out ]

# The screen for selecting the contents of the editing channel

# to be printed.

# 1)	At first, check the channel no. to be printed.

# 2)	Move the cursor to the articles to be printed with the

numeric keys or the arrow keys and press the [INS] key.

# 3)	A “*” mark will be displayed next to those items.

Press [INS] key once more to cancel.

# Multiple articles can be marked.

# 4)	Pressing the [ENTER] key after selecting all the items to

# be printed.

The message “print out (y=0 / n=1)?” appears.

Select “y” and printing starts.  Select “n” and the screen returns to [Fig 1-1 Data].

# 4.4.2.  Selecting Channel Number to be printed

# The channel number set in [Fig 2. Editing Channel Selection]

# 4.4.3.  Contents

# 1)	 all :  from 2) to 8)

# 2)	 Parameters: Mechanical Parameters

# 3)	 Drawing Names in current block #33

# 4)	 Working Specifications of current channel

# 5)	 XYZ data of current channel

# 6)	 FPB. data of current channel

# 7)	 Elongation Measurement file of current channel

# 8)	 S.B. compensation file of current channel

5.1 Plan   ( Short Cut Key :  F2  )

[ Fig 5-1 Working Channel Selection ]

Press [2] and then the [ENTER] keys at fig 0-6 Main Menu.

Screen [Fig 5-1 Working Channel Sselection] is displayed.

- Block name: Input a name for the group of 20 channels in the

memory, that clearly describes the product.

This block name is saved with the data when

saved to a floppy disk as well..

- Plan		: Production schedule

- Channel 	: The drawing names of 20 channels in the

memory are displayed below.

- Item  :  Working order if using the counter option.

- Current work setting :

[*] mark indicates the item is the current working channel.

Move the cursor to the item you want to revise with the [ENTER] key or with the arrow keys and input the

quantity to be produced.  “Done” items should be marked zero.

# Press the [INS] key to make an item the current working channel.

# 5.2  Change: Deciding whether to edit the schedule or not.

Change ? (y=0/n=1)     y / n

yes : To change the current working channel.

no :  To not change the current working channel.

# Use the left/right directional keys and [ENTER] to select

“yes” or “no”.  [0] instead of “y” and [1] instead of “n” can also be used.

Caution!  You must set and save the working channel again after you revise the data of the channel already set.

5.3.  Case of selecting “yes” at the message “Change ? (y=0/n=1)     y / n”

Press [0] and the [ENTER] key or select “y” with the left/right arrow keys.

The cursor moves to the column “name”.

Input a block name you want.

Move the cursor to the item you want to revise by pressing the [ENTER] key or by using the arrow keys and

then input the quantity,

Mark “done” items “0” and then press the [INS] key.

Then the [*] mark is displayed by the item number you selected and it is designated the current working

channel.

After that, press the [ESC] key and the message  “save changes ?   y / N “  is displayed at the

bottom of the screen.

Select “y” and the message “save changes   yes” is displayed at the bottom of the screen.

Then press the [ENTER] key.  The message “plan saved” is displayed at the bottom of the screen.

# Press [ENTER] or [ESC] to quit this screen.

5.4. Selecting “no” at the message “Change ? (y=0/n=1)     y / n”:

The display returns to the screen [Fig 0-6 Main Menu].

# 6.  Operation

# 6.1. Preparation

(see section 4.0.)	Turn on the main power.

Turn on the power switch of the controller.

Turn on the motor switch.

Pressing [ENTER] three times at [Fig 0-1 Startup Screen].

The screen changes to [Fig 0-6 Main Menu] after checking the origin.

(see section 5.1)	Set working channel in [Fig 5-1 Working Channel Selection].

# 6.2  Operation Mode

# Manual Mode:  Press [3] and [ENTER] or select [Manual] with the left/right arrow keys at the

screen [Fig 0-6 Main Menu]. [Fig 6-1 Manual Mode] is displayed.

The [MANUAL] key on the control panel can also be pressed.

# Jog Mode :  Press [JOG] key on the control panel in Manual mode.

# Auto Mode:   Press [AUTO] key on the control panel screen [Fig 6-2. Auto Mode] is displayed.

# Step Mode : Press [STEP] key on the control panel screen [Fig 6-2. Step Mode] is displayed.

# Elongation Mode : Selecting [4] or [Elong] with the arrow keys and the [Fig 6-3 Elongation Measurement]

screen appears. Auto mode must be selected beforehand. If [4] or [Elong] is selected while in manual

mode, the message “in manual run, elong not allowed!!  [ret]“ appears.

6-3  Operation Monitoring Screen

[ Fig 6-1  Manual Mode ]

# 1) item : the item no. set in working channel selection.

Marked with [*].

# 2) channel :the channel number of the present working

# channel

# 3) style : working style (Process or Full)

# 4) channel name

# 5) process# : process number in operation

6) done    : worked quantity/ setting quantity

7) speed   : speed

8) data    : setting value

# 9) current  : present position

# 10) dir (direction) : direction in jog mode.

# 6.4.  Manual Mode

# 1) Origin check

# Determines the mechanical origin

# 2) Pipe set position

# Moves the chuck carriage to the pipe set position

This key can be used after setting the pipe set position in auto mode.

# 3) Axes operation

# Jog Mode ON

With Jog Mode ON, movements have no relation to the data from the channel.

Movement along the axes can be executed by pressing and holding the axes buttons.

Feed forward	:  To move the chuck carriage forward along the feed axis.

Feed back   	:  To move the chuck carriage backwards along the feed axis

Plane left   	:  To rotate the plane axis counter-clockwise from the point of view of the

operator.

Plane right  	:  To rotate the plane axis clockwise from the point of view of the operator.

Bend  		:  To bend

Return 		:  To return the bending arm to the bend origin.

# Jog Mode OFF

In Jog Mode OFF, the manual execution of the working channel data is available.

Movement along the axes can be achieved by pushing an axes button once to achieve movement in the

set increment.

# 4) Cylinder Operation

- The switches are toggled. That is, if pushed once, it is closed and if pushed one more time, it is open.

- When the cylinder is closed, the lamp of the key is on.

When the cylinder is open, the lamp of the key is off.

Chuck	: on-hold / off-release

Clamp  	: on-hold / off-release  	It is not available when crossmove is on or closed.

That is, when crossmove quits the center line of the bending form.

Table	: on-up / off-down 		It is not available when crossmove is on or closed.

That is, when crossmove quits the center line of the bending form.

Mandrel 	: on-forward / off-backwards

Crossmove: on-close 		When crossmove quits the center line of the bending form.

off-open 		When crossmove is on the center line of the bending form.

It is not available when clamp or pressure is closed.

Pressure	:on-hold / off-release 	It is not available when crossmove is on or closed.

That is, when crossmove quits the center line of the bending form.

SUPP. 1 	: on-up / off-down		It indicates support for bending taking place at the R1(upper) mold.

SUPP. 2	: on-up / off-down		It indicates support for bending taking place at the R2(lower) mold

6.5.  Auto Mode Operation			           [ Fig 6-2  Auto Mode ]

1) Pressing [AUTO] key on the control panel, the screen,

[Fig 6-2 Auto Mode], is displayed.

# The chuck carriage then automatically moves to the pipe

set position of the channel set in current working channel

selection.  All output devices(cylinders) are ready to

execute the first process.

2) After that, the lamp of the [START] key is turned on

indicating all preparations are complete.

Insert a pipe in the chuck carriage and then press the

[START] key.

3) During operation, the relative values of the current

positions are always displayed. These relative values are

based on the starting position of that process.

4) When a bending is complete, unload the pipe through the means of discharge you set in the working

specifications.

After the discharge is complete, the chuck carriage returns to the pipe set position again for the next bending.

After that, the lamp of the [START] key lights again.

5) If any interference takes place in auto operation, revise squeeze type of FPB data and then make a trial run.

6) Lap-Time: This indicates the time for a bending from the time of pressing the [START] key to the time the

message, “step on foot switch1!” or “next piece ? [START]” appears.

That is, the processing time for a bending.

6.6.  Step Mode Operation

# This mode executes a bending step by step.

1) The step operation monitoring screen is the same as the auto mode screen.

2)	Press [STEP] key on the control panel.  Chuck carriage automatically moves to the pipe set position

of the channel set in the current working channel selection.

All of output devices(cylinders) are ready to execute the first process.

3) After that, the lamp of the [start] switch is turned on.  This means that all preparation are complete.

Insert a pipe in the chuck carriage and then press the [START] switch.

4) During operation, the relative values of the current positions are always displayed.

These relative values are based on the starting position of that process.

5) When a step is complete, the lamp of [START] key is turned on again and the brief name of next step is

displayed at the bottom of the screen.  Press the [START] switch again to execute the next step.

You can finish a bending by pressing the [START] switch repeatedly.

6) Switching between auto mode and step mode

- If the [STEP] key is pressed during a run being executed in auto mode, the mode is converted to step

mode after the current process is finished.

- If the [AUTO] key is pressed during a run being executed in step mode, the mode is converted to auto mode

immediately.

7) Switching between auto mode and manual mode

- If the [MANUAL] key is pressed or [MANUAL] is selected from the on screen menu during a run being

executed in auto mode, the mode is converted to manual mode after the current process finishes.

- After switching to manual mode, if the [AUTO] key is pressed immediately, without the execution of any

operation or any editing, the current run can be continued in auto mode.

8) Messages in Step Mode Operation

STEP_xx crossmove on	[start]		STEP_xx crossmove off  	[start]

STEP_xx	pressure  on	[start]		STEP_xx pressure	off	[start]

STEP_xx clamp    on	[start]		STEP_xx clamp	off	[start]

STEP_xx mandrel  on	[start] 		STEP_xx mandrel	off	[start]

STEP_xx table	up  	[start]		STEP_xx table 	down	[start]

STEP_xx	chuck   	on  	[start]		STEP_xx	chuck	off	[start]

STEP_xx	support 	1 	[start] 		STEP_xx	support 	2 	[start]

STEP_xx	support 	3      	[start] 		STEP_xx	return 	1  	[start]

STEP_xx	return 	2      	[start] 		STEP_xx	return 	3  	[start]

STEP_xx return 	4      	[start] 		STEP_xx feed 	1  	[start]

STEP_xx	feed 	2      	[start] 		STEP_xx	feed 	3  	[start]

STEP_xx feed 	4      	[start] 		STEP_xx feed 	5  	[start]

STEP_xx plane 	1      	[start] 		STEP_xx	plane 	2      	[start]

STEP_xx	bend 	1      	[start]  		STEP_xx bend 	2      	[start]

9) Differences between the operation of the [START] key on the controller’s main control panel and the

[START] switch on external operating panels.

[START] key on the control panel 		:If pressed once, a function is executed.

Holding it continually has no effect.

External [START] switch on the operating panel	:Continues to repeat the function continuously as long. As

the key is depressed.

6.7.  Elongation Measurement Mode                     [ Fig 6-3. Elongation Measurement ]

Select [4] or [ELONG] with the arrow keys.

A screen [Fig 6-3 Elongation Measurement] appears.

Auto mode must be enabled beforehand.

# If [4] or [ELONG] is selected in manual mode, the mess-

# age “ in manual run, elong not allowed !!  [ret]“ appears.

1) The elongation length and rate are measured, and the

results can be saved for reference.

2) The lamp of the [START] switch is turned on.

This indicates that all preparations are complete.

Insert a pipe into the chuck carriage and then press the

[START] switch.

3) During operation, bend angles, calculated arch lengths,

actually used pipe lengths and rates of each process are displayed.

4) When a process is over, the lamp of the [START] key is turned on again.

Press the [START] switch again to make another measurement.

5) You can quit the measurement mode after at least two operations.

6) inquiry of saved data

At the bottom of the screen, [Fig 6-3 Elongation Measurement],

Select “y” at the message, “view elong data?       y/n “,  the saved measurements are displayed.

Press [ESC] at the message, “to exit               [esc]”,

Select “y” at the message “measure elongation ?   y/n “.  See section 7) measuring.

If “n” is selected, the screen returns to the screen [Fig 6-1 Operation].

7) measuring

Select “n” at the message “view elong data?       y/n “.

Select “y” at the message “measure elongation ?   y/n “.

The message “To continue measuring, press [start]” appears.

Then press the [START] key. ([AUTO] or [STEP] modes depending on the previous mode)

After two measurements press the [ESC] key at the message, “to exit               [esc]”.

At the message “Save measurements?    y/n “ select “y” or “n” and then quit by pressing [ESC].

8) items

bend    	:  bending angle

ⓐ calc (mm)     :  calculated arch length that depends on the radius and bend angle

ⓑ measured (mm) :  pipe length actually used for bending

ⓒ elongation     :  elongated pipe length at bending (not displayed)       ⓒ = ⓐ - ⓑ

ⓓ rate(%)        :  ⓓ = { ⓐ - ⓑ }  / ⓐ x 100

# 6.8.  Mode Switching

# 1)  Mode switching is possible between the three modes (auto, step and manual)

Switching to elongation mode is possible from auto mode

Switching to manual jog mode is possible from manual mode.

# 2)  Editing is available in any operation.

# 3)  It is always possible to switch from manual mode to auto or step mode.

# 4)  Switching from auto or step mode to manual mode is possible as soon as the current process ends.

# 7. Emergency Stop

# 1) Limit switch

# Emergency

When the bend and feed axes exceed their preset limit a system errors is caused, and

the motor for the hydraulic system is turned off, and the servo system is disabled(inactive, servo-off).

Recovery :

Return the axes to their proper position.

Turn off the motor switch on the control panel and then turn it on again.

The system then returns to manual mode.

# 2) Emergency Stop Switch

# Emergency

When normal operation is impossible for any reason, press the emergency stop switch.

The motor for the hydraulic system is turned off, and the servo system is disabled(inactive, servo-off).

Recovery :

Correct the cause of the error and then release the emergency switch.

Turn off the motor switch on the control panel and then turn it on again.

The system then returns to manual mode.

# 3) Servo Alarm

# Emergency

When normal operation is impossible due to a servo alarm, the motor for the hydraulic system is

turned off and the servo system is disabled(inactive, servo-off).

Recovery :

Turn off the servo pack and then turn it on again after a few minutes.

Then turn off the motor switch on the control panel and turn it on again.

# 8. Errors and Recovery

# 1) Feed Data Error

================================================================================

[Message]                       	[Meaning]

================================================================================

Pressure interference,   correct, [Enter]	Interference between carriage and pressure

Bend form interference,  correct, [Enter]	Interference between carriage and bending form

Feed range over,       correct, [Enter]	The target feed position is under zero.

================================================================================

Solution:   1. Press [ENTER] to erase the error message.

2. Review and revise feed data of FPB data and 6) pipe set position, 7) pressure interference

position, 8) bending form interference position of working specifications.

3. Set the channel again in Plan screen and run.

# 2) Bend Data Error

================================================================================

[Message]                       	[Meaning]

================================================================================

Bend range over,	correct, [Enter]	 	A bend angle is over 190˚.

================================================================================

Solution:   1. Press [ENTER] to erase the error message.

2. Review and revise bend data and spring back data of the FPB data.

The sum of bend data and spring back data should be less than 190˚.

3. Set the channel again in Plan screen and run.

# 3) In/Out Devices Error

================================================================================

[Message]                       	[Meaning]

================================================================================

Chuck abnormal,	    correct, [Enter]

Crossmove abnormal,  correct, [Enter]	A normal operation of each cylinder system is impossible.

Pressure abnormal,    correct, [Enter]	The solenoid valve or cylinder or sensor is malfunctioning.

Clamp abnormal,     correct, [Enter]		Related parameters are not proper.

Mandrel abnormal,    correct, [Enter]

Table abnormal,      correct, [Enter]

================================================================================

Solution:   1. Press [ENTER] to erase the error message.

2. Check if the related sensors are at the proper on/off position or not.

Check if the related sensors are functional or not.

3. If any problem or fault is not discovered, check the cylinder and solenoid valves and relays by

pressing the related cylinder key in manual mode.

4. If the sensors is malfunctioning and there are no spare sensors, the system can be operated

by setting “N” for the related sensor use or non-use in mechanical parameters setting.

However, the sensor should be changed as soon as possible for maximum efficiency.

5. If the problem is not a sensor, the malfunctioning part should be repaired immediately.

# 9. Emergency Stop & Recovery

# 1) Limit switch & Emergency Stop

================================================================================

[Message]                       	[Meaning]

================================================================================

[f  :    ] error, correct error & [home] 	Feed origin limit

[ f :     ] error, correct error & [home] 	Feed end limit

[  b:    ] error, correct error & [home] 	Bend end limit

[   :   e] error, correct error & [home] 	Emergency switch is pushed.

Motor turned off 			    	Motor switch is turned off.

================================================================================

Whenever normal operation is impossible due to any reason, the emergency stop switch is pressed, or the bend

and feed axes run over their preset limits causing a system error, the motor for the hydraulic system is turned off

and the servo system is disabled(inactive,servo-off).

Solution:	1. Use the error message to confirm the cause of the error.

# 2. Correct the cause of the error and release the emergency switch.

Return the axes to their proper position.

3. Turn off the motor switch on the control panel and then turn it on again.

4. Press [ENTER] key to erase the error message.

The system then returns to manual mode.

5. Reset the mechanical origin with [Origin] key in manual mode.

The system should be completely recovered.

# 2) Servo Alarm

================================================================================

[Message]                       	[Meaning]

================================================================================

[   :f   ] error, correct error & [home] 	feed servo alarm  (over load)

[   : p  ] error, correct error & [home] 	plane servo alarm  (over load)

[   :  b ] error, correct error & [home] 	bend servo alarm  (over load)

================================================================================

Emergency

When normal operation is impossible due to a servo alarm, the motor for the hydraulic system is

turned off and the servo system is disabled(inactive, servo-off).

Solution:	1. Correct the cause of the servo alarm.

2. Turn off the servo pack and turn it on again after a few minutes.

# 3. Turn off the motor switch on the control panel and then turn it on again.

4. Press [ENTER] to erase the error message.

5. Reset the mechanical origin with [Origin] key in manual mode.

The system should be completely recovered.

# Appendix 1-1:  Sequences in Squeeze

# Working style : Full

| Feed squeeze 1 1. feed (feed+feed squeeze), return 2. plane 3. feed (feed squeeze) x (-1) 4. bending | Feed squeeze 2 1. feed, plane, return 2. clamping 3. unchucking 4. feed (feed squeeze) x (-1) 5. chucking 6. bending |
| --- | --- |
| Plane squeeze 1 1. feed , return 2. plane 3. bending |  |
| Bend squeeze 1 1. feed, return to squeeze data, plane 2. return 3. bending | Bend squeeze 2 1. feed, return, plane 2. bending squeeze data 3. pressure off 4. pressure on 5. bending |

# Working style : Process

| Feed squeeze 1 1. chucking 2. unclamp 3. return 4. feed (feed data+squeeze data) 5. plane 6. feed back (squeeze data) 7. clamping 8. unchucking 9. pressure holding 10. feed back (next feed data) 11. bending | Feed squeeze 2 1. chucking 2. unclamp 3. return 4. feed (feed data+squeeze data) 5. plane 6. clamping 7. unchucking 8. feed back (feed data) 9. pressure holding 10. bending |
| --- | --- |
| Plane squeeze 1 1. feed, return 2. plane 3. bending |  |
| Bend squeeze 1 1. feed, return to squeeze data , plane 2. return 3. bending | Bend squeeze 2 1. feed, return, plane 2. bending squeeze data 3. pressure off 4. pressure on 5. bending |

# Appendix 2:  Sequences in complicated squeezes

# Working Style : Full

==================================================================================================

Squeeze (Feed, Plane, Bend)	       (0,0,0)    (1,0,0)     (0,1,0)     (0,0,1)    (0,1,1)    (1,0,1)     (1,1,0)     (1,1,1)

==================================================================================================

1   Bend Return Squeeze     1					0	0	0		0

2   Feed  or  Feed Squeeze  1		0	0	0	0	0	0	0	0

3   Bend Return 			0	0	0				0

4   Plane				0	0		0		0

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Target checking of  2. Feed.		0	0	0	0	0	0	0	0

Target checking of  4. Plane.		0	0		0		0

Target checking of  3. Bend Return.	0	0	0				0

------------------------------------------------------------------------------------------------------------------------------------------------------------------------

# 5   Bend Return Squeeze 1” & Target checking			0	0	0		0 -------------------------------------------------------------------------------------------------------------------------------------------------------------------------

6   Plane & Target checking				0		0		0	0

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------

7   Feed Squeeze 1” 	& Target checking		 0				0	0	0

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------

8   Feed Squeeze 2   & Target checking 				in case feed squeeze 2 is set.

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------

9   Bend  or Bend Squeeze 2		0	0	0	0	0	0	0	0

& Target checking

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------

10  Bend Squeeze 2” & Target checking 				in case bend squeeze 2 is set.

# Working Style : Process

==================================================================================================

Squeeze (Feed, Plane, Bend)	       (0,0,0)    (1,0,0)     (0,1,0)     (0,0,1)    (0,1,1)    (1,0,1)     (1,1,0)     (1,1,1)

==================================================================================================

1   Bend Return Squeeze     1					0	0	0		0

2   Feed  or  Feed Squeeze  1		0	0	0	0	0	0	0	0

3   Bend Return 			0	0	0				0

4   Plane				0	0		0		0

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Target checking of  2. Feed.		0	0	0	0	0	0	0	0

Target checking of  4. Plane.		0	0

Target checking of  3. Bend Return.	0	0	0				0

------------------------------------------------------------------------------------------------------------------------------------------------------------------------

5   Plane 						0		0		0	0

------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Target checking of  5. Plane.				0	0	0	0	0	0

Target checking of  1. Bend Return Squeeze				0	0	0		0

------------------------------------------------------------------------------------------------------------------------------------------------------------------------

6   Bend Return Squeeze 1” & Target checking			0	0	0		0

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------

7   Feed Squeeze 1” 	& Target checking		 0				0	0	0

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------

8   Feed Squeeze 2   & Target checking 				in case feed squeeze 2 is set.

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------

9   Bend  or Bend Squeeze 2		0	0	0	0	0	0	0	0

& Target checking

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------

10  Bend Squeeze 2” & Target checking 				in case bend squeeze 2 is set.

# Appendix 3: Mechanical Parameters

===============================================================================

parameter       	    mm or msec          remark

===============================================================================

1.Machine        ______     SP-15HT   	Machine name

2.Total feed        ______        1500 	Distance from feed origin to bending form.

It can be changed by changing the position of the feed origin sensor.

It is only for use during manual operation not during auto run.

3.Aft feed          	______	N	not presently available.

4-18  Speed level of axes		To set the speed levels, from 0 to 4, for each axis.

19.Supporter position	______     800 	Distance from feed origin to supporter position.

It can be changed by changing the position of the feed origin sensor.

20.Supporter delay	______     300 	Delay time before supporter operation in 1st process.

21.Clamp open time	______       0 	Interval between the start of the unclamping step and the beginning of the next step.

22.Clamp close time 	______       0 	Interval between the start of the clamping step and the beginning of the next step.

23.Clamp close delay	______       0	Delay time before clamping step starts.

24.Clamp,press delay 	______	N	not presently available.

25.Chuck open time   ______       0	Interval between the start of the unchucking step and the beginning of the next step.

26.Chuck close time	______       0	Interval between the start of the chucking step and the beginning of the next step.

27.Chuck delay	______       0	Delay time before a chucking or unchucking step starts.

28.Feed delay	______       0	Delay time before feed step starts.

29.Feed origin return time___	N	not presently available

30.Plane delay	______       0	Delay time before plane step starts.

31.Plane origin return time___	N	not adopted.

32.Bend delay	______       0	Delay time before bend step starts.

33.Bend return delay	______       0	Delay time before bend return step starts.

34.Pressure open time	______       0	Interval between the start of the pressure-open step and the beginning of the next

step.

35.Pressure close time	______       0	Interval between the start of the pressure-close step and the beginning of the next

step.

36.Pressure half open time___	  50 	Time to stop opening after pressure-open step starts.

If this parameter is not “0”, the pressure doesn’t get entirely opened.

That is, pressure opening stops after this time.

If the crossmove option of the next seq. is “yes” or the carriage feed forward to the

pressure interference position in the next sequence , pressure is opened entirely in no

relation to this parameter.

37.Pressure half close time____    200	This parameter can be used to close pressure half in advance before feed in the 1st

process of NGP style.

Time to stop closing after pressure close step starts in the 1st process of NGP style.

If this parameter is not “0”, the pressure doesn’t get closed entirely.

That is, pressure closing stops after this time.

If the carriage feed forward to the pressure interference position in the next

sequence or the current position of the carriage is greater than the pressure

interference position, this parameter is not effective.

38.Pressure half to end close time	 200	Time to close entirely in case pressure is stopping in the middle of the cylinder.

39.Crossmove off time	______       0	Interval between the start of crossmove-off (opening) step and the beginning of the

next step.

40.Table up time   	______     200	Interval between the start of the table-up step and the beginning of the next step.

41.Table down time	______     200	Interval between the start of table-down step and the beginning of the next step.

42.Mandrel lubricant time ___	 800	Mandrel lubricating time

43.Mandrel time	______   	 500	Interval between the start of the mandrel-on/off step and the beginning of the next

step.

44.Crossmove delay	______       0	Delay time before crossmove-on/off step starts.

45.Corssmove on time	______    1000	Interval between the start of crossmove-on step and the beginning of the next step.

46.Table down delay	_____        0	Delay time before table-down step starts.

When table goes down to R2 from R1, the chuck carriage quits bending form

before table-down step. This is a crossmove-on step.

If the bending degree of the previous process is greater than 90˚, the bending form

interferes with movement of the bent pipe at this crossmove-on step.

To remove the interference, it is necessary to delay crossmove-on step until feed step

is finished. This parameter is very useful to do so.

But if the bending degree of the previous process is smaller than 90˚, the bending form does not interfere with the movement of bent pipe at this crossmove-on step.

Therefore this parameter is not effective when the bending degree of the previous

process is smaller than 90˚

47.Die change speed	______	N	not presently available

48.Table up delay 	_____       0	Delay time before table-up step starts.

When table goes up to R1 from R2, the chuck carriage quits bending form before

table-down step. This is a crossmove-on step.

If the bending degree of the previous process is greater than 90˚, the bending form

interferes with the movement of bent pipe at this crossmove-on step.

To remove the interference, it is necessary to delay crossmove-on step until feed step

is finished. This parameter is very useful to do so.

But if the bending degree of the previous process is smaller than 90˚, the bending form does not interfere with the movement of the bent pipe at this crossmove-on step.

Therefore this parameter is not effective when the bending degree of the previous

process is smaller than 90˚

49.Booster time	_____	N	not presently available.

50.Discharge time    ______    3000	Interval time between unclamping step and bend-return step to take the pipe out

after final bending.

This is effective under the discharge option “2” in working specifications.

51.Table position	______	N	not presently available

52.Seam checker time	______	N	not presently available

53.Sensor check delay	______    100	Sensor checking time for all of the sensor on the output devices.

Reduce this parameter if the speed of the cylinder is set fast.

Raise this parameter if the speed of the cylinder is set slow.

If the speed of the cylinder is slow and this parameter is too small to check the sensor,

it may cause a cylinder error.

Likewise, if the speed of the cylinder is too fast and this parameter is too big,

It may cause some time loss.

==================================================================================================

54.Crossmove sensor 	______ 	Y/N	1.  Set this option if the cylinder is equipped with sensors in order to monitor

its operation.

55.Pressure sensor  	______	Y/N

2.  If a cylinder is not equipped with sensors and this parameter is set as “y”,

56.Clamp sensor  	______	Y/N	    it causes a cylinder error.

57.Mandrel sensor    ______	Y/N	3.  You can run the machine by setting this parameter to “n” on purpose,

even if the cylinder is equipped with sensors.

58.Table sensor	______	Y/N	    To do so, it may be necessary to change some parameters.

59.Chuck sensor      ______	Y/N

60.Plane origin sensor	______	Y/N       Set this to “y” if you need plane origin.

# Appendix 4:  Monitoring Screen for inputs and servo axis.

Pressing [3] and [ENTER] at [Fig 0-2. Parameter Setting], a screen [Fig 10. Monitoring Screen] is displayed.

When any error occurs and the cause can not be found this monitoring screen may be very useful in diagnosing

the problem.

1) Servo Axis Test				  	       [ Fig 10. Monitoring Screen ]

- Turn off the [MOTOR] switch on the control panel.

- Compare the value on the screen with actual movement by

hand.

- If there is any difference, check the servo system.

2) Key Input Test

- When a key on the control panel is inactive, check it with

this function.

- In this screen, any actual operation is impossible.

- Pressing any key, a number is displayed in the right hand

column. If the number does not match the number shown in

[Ffig 10-1]. The cause is an internal controller malfunction.

# [ Fig 10-1. Key number ]

================================================================================

CLAMP		01	CROSSMOVE	02	TABLE		03	PRESSURE	04

SUPP.1       	05    	SUPP.2 		06

MANUAL	09     	JOG		10	AUTO		11	STEP           12

START       	13     	CHUCK         14	MANDREL    	15

ORIGIN      	17     	P.S.P       	18	FEED FW     	19	FEED BW       20

PLANE  R    	21     	PLANE  L 	22	BEND        	23     	RETURN		24

================================================================================

3) Input Test

- Check if the input signals are normal.

- Sensors, external switches and servo alarm are all included in the inputs.

- When an input device is normal and the signal is received by the controller, a [o] will be displayed under the

input number in [Fig 10-2. Input Number].

[ Fig 10-2  Input Number ]

================================================================================

x-move origin sensor     00,02	x-move end sensor	      01,03

pressure origin sensor	04	pressure origin sensor	05

table up sensor	      06,08	table down sensor	      07, 09

clamp sensor         	11    	chuck sensor		12

mandrel origin sensor	13	mandrel end sensor		14

feed decel. Sensor		15	feed origin sensor      	16

plane origin sensor    	17	bend decel. Sensor		18	bend origin sensor		19

motor switch        	20	external start switch	21	foot switch 1      	22

foot switch 2     		23	emergency switch		24

feed origin limit		25	feed end limit    		26	bend limit     		27

feed servo alarm       	29	plane servo alarm 		30 	bend servo alarm 		31

# Appendix 5:  Internal Connection of Controller

[ CPU Board ]

[ In / Out Board ]

[ Servo Control Board ]

[ AC Power Connection in Controller ]

# Text boxes

Input  0         Input  1          Output  0        Output  1

FEED            PLANE             BEND            N.C.

Monitor     Key        Printer               N.C.

Panel                                            AC

DC&Key                  F.D.D.             N.C.          Power Inlet

Key Panel Connector ( 12P )

FDD DC Power  ( 4P )

Buzzer

Monitor                        Controller       Fan

Connector(Female)

Connector

Connector(Male)                                      (F)   (M)

Power

Switch                                                                MCCB